The State Building Code will be updated during the 2010 Legislative Session.  Procedurally this is accomplished by adoption of Legislative Rule, Title 87, Series  4, State Building Code, by both the House of Delegate and the State Senate, after approval by the Joint Legislative Rule Making Committee. 

	The State Fire Commission approved unanimously adoption the following ICC and NFPA standards as the State Building Code:

			2009 IBC		2008 NFPA 70 – National Electric Code
                     		2009 IRC		2009 NFPA 101 – Life Safety Code
                                            2009 IEBC
                                                                                       ICC/ANSI A117.1/ 2003 is unchanged
                                            2009 IPC
 			2009 IMC
 			2009 IFGC
			2009 IECC
			2009 IPMC

                The new editions were adopted WITH FIRE COMMISSION AMENDMENT.  However, all the 2006 amendments adopting the 2003 I Codes remain in the Legislative Rule. The major items include:

1. Chapter 11 of the IRC (Energy Efficiency) is deleted from the 2009, but unlike in 2006 it WAS NOT 
    replaced. The net effect is the 2009 IECC will govern energy efficiency in both commercial and 
    residential uses.

2. IRC 2009 will require residential sprinklers  in 2011.

3. IBC 2009 deletes Section 101.4.5 referencing the International Fire Code.

4. IEBC 2009, Section 101.4.2 deletes International Fire Code and replaces it with NFPA 101/2009 Life 
    Safety Code.

5. The Legislative Rule did not change Group U, Utility structure and store shed inspection and permits exemption size from 150 in the Rule to 200 in the Code, creating a conflict. The Rule can’t be more restrictive than the Code (statute).

You can download the Legislative Rule from the Secretary of State’s web site:

www.wvsos.com/adlaw/modified/modifiedrules.htm.  Scroll down to  “Title/Series” 87-4